August 17, 2006

ENVIRONMENTAL SCIENCE

Metal Pollution From Medieval Mining Persists

Study looks at patterns of heavy-metal contamination of a site in

southern France

Rebecca Evanhoe

Scientists have tracked down the source of high levels of heavy metal

pollution at a site in southern France: medieval metallurgical

workshops. Sandrine Baron, Jean Carignan, and Alain Ploquin of the Center for

Petrographic and Geochemical Research in Nancy, France, report that the

lead, antimony, arsenic, copper, and zinc residues left behind there

more than 800 years ago still pose a potential health threat (Environ.

Sci. Technol., DOI: 10.1021/es0606430). Mont-Lozère Massif, the site of

medieval workshop remnants that they studied, is in the Cévennes National

Park, where people fish, hunt, farm, and camp.

Heavy metals are distributed in the environment because of natural and

anthropogenic mechanisms. The trick for Baron's team was to figure out

to what extent each mechanism contributed. While it's not surprising

that large quantities of heavy metals have staying power in soil and

rocks, this study is one of the first to systematically attribute

present-day pollution levels to an ancient source of man-made pollution. The

study "certifies the responsibilities of the polluters and the origin of

the toxicity," Baron points out.

The team examined leftover slag-the by-product of smelting ore to

purify mined metals-and the background content of the metals in surrounding

soil and granite. By comparing the lead-isotope ratios found in the

slag to those found in rock and soil, Baron's team illustrated that binary

mixing between slag and granite was the primary method of dispersion

and verified that the medieval pollution contributed at least 40% of the

lead found in the granite.

"Studies of old metallurgical pollution allow the understanding of

modern pollution because we can observe the long-term effect of heavy

metals in the environment," Baron says. He hopes that this research will

continue to elucidate historical anthropogenic pollution by examining what

he calls environmental archives, such as peat bog cores and lake

sediments. He stresses that further studies will require an interdisciplinary

approach, with collaboration between geochemists, archaeologists,

historians of science, and toxicologists.

Chemical & Engineering News

ISSN 0009-2347

Copyright © 2006 American Chemical Society